## Slide 1
WaferLLM Inference on WSE-3
Prefill · Decode · End-to-End Throughput
Re-implementation and Verification

## Slide 2
Test Case Configuration
Each JSON file defines one (Model, Grid) benchmark
{ "P": 660, "bsz": 1, "dim": 8580, "seq_len": 4620, "ffn_dim": 29700, "n_heads": 1, "n_kv_heads": 1, "head_dim": 8580, "layer_num": 80, "group_num": 22 }
P = 660
660×660 PE grid on WSE-3 (435,600 cores)
bsz = 1
One inference request at a time
dim = 8580
Hidden dim: ceil(8192/660)×660 [Qwen2-72B actual: 8192]
seq_len = 4620
Input tokens ~4096: ceil(4096/660)×660
ffn_dim = 29700
FFN intermediate: ceil(29568/660)×660
n_heads = 1
Merged to 1 head — preserves matrix sizes, simplifies distribution
head_dim = 8580
Equals dim since n_heads=1
layer_num = 80
Transformer layers — scales single-layer time to full-model TPR
group_num = 22
Allreduce groups for decode attention reduction (660/22=30 PEs/group)
All dimensions rounded to nearest multiple of P → equal work per PE, no remainder

## Slide 3
Prefill
Processing the input prompt — all tokens at once
Transformer Layer
RMSNorm → Q/K/V Projection → RoPE → Attention → Output Proj → RMSNorm → FFN (up / gate / down)
Dimension Selection (LLaMA3-8B, P=480)
seq_len
ceil(4096 / 480) × 480
= 4,320
input tokens rounded to multiple of P
dim
ceil(4096 / 480) × 480
= 4,320
hidden dim rounded to multiple of P
ffn_dim
ceil(14336 / 480) × 480
= 14,400
FFN dim rounded to multiple of P
Cycle Count → TPR
Measured via hardware cycle counter Max over all PEs (slowest PE = wall-clock time) Averaged over 50 runs, 5 warmup
Time/layer = cycle_count / 1.1×10⁹ TPR = seq_len / (time_s × layer_num)
Example — LLaMA3-8B, P=480
Max cycle count:
6,495,367.7
Time per layer:
6,495,367.7 / 1.1×10⁹ = 5.905 ms
TPR:
4,320 / (5.905×10⁻³ × 32) = 22,862 tok/s
Why TPR is seq_len-independent: FFN time ∝ seq_len, so TPR = seq_len/(C·seq_len) = 1/C (constant)

## Slide 4
Decode
Generating new tokens one at a time
How Decode Works
Each step generates exactly 1 new token. The new token attends over ALL previous tokens stored in the KV cache.
Q = new token projected → shape (1 × dim) K_cache = all past Keys → shape (seq_len × dim) V_cache = all past Values → shape (seq_len × dim) scores = Q × Kᵀ → output = scores × V
Why seq_len = KV cache size
Prefill writes one K,V pair per input token into the cache. When decode begins, the cache holds seq_len entries. Decode reads ALL of them every step → performance scales with context length.
seq_len = context window ≈ 4096, rounded up: ceil(4096/P)×P
Cycle Count → TPR (Decode)
Input is always 1 token → TPR formula changes:
Time/layer = cycle_count / 1.1×10⁹ TPR = 1000 / (time_ms × layer_num)
vs Prefill: TPR = seq_len / (time_ms×10⁻³ × layer_num)
Example — LLaMA3-8B, P=420
Max cycle count:
16,373.1
Time per layer:
16,373.1 / 1.1×10⁹ = 0.01488 ms
TPR:
1000 / (0.01488 × 32) = 2,099.5 tok/s
Prefill
Decode
Tokens/pass
seq_len
1
TPR formula
seq_len/(t×L)
1000/(t_ms×L)
seq_len role
input length
KV cache size

## Slide 5
End-to-End Throughput
Combining prefill and decode into a single user-facing metric
E2E = new_tokens / ( input_tokens / prefill_TPR + new_tokens / decode_TPR )
denominator = total wall-clock time of the full request
Phase 1 — Prefill
time_prefill = input_tokens / prefill_TPR
e.g. 4096 / 27,923 = 0.147 s
Phase 2 — Decode
time_decode = new_tokens / decode_TPR
e.g. 128 / 2,256 = 0.057 s
Example — LLaMA3-8B, 4096in / 128out
Prefill TPR = 27,923 tok/s (660×660) Decode TPR = 2,256 tok/s (360×360)
E2E = 128 / (4096/27,923 + 128/2,256) = 128 / (0.1467 + 0.0567) = 128 / 0.2034 = 629.2 tok/s
E2E is always lower than both prefill and decode TPR individually — you pay the cost of both phases.

## Slide 6
E2E Results vs Paper
LLaMA3-8B (660×660 prefill + 360×360 decode) | LLaMA2-13B (750×750 + 375×375)
Model
Scenario
Ours (tok/s)
Paper (tok/s)
Diff
LLaMA3-8B
2048in / 128out
747.9
764.4
−2.2%
4096in / 128out
629.2
604.4
+4.1%
2048in / 2048out
2,036
2,370
−14.1%
4096in / 4096out
2,087
2,459
−15.1%
LLaMA2-13B
2048in / 128out
499.7
473.9
+5.4%
4096in / 128out
470.0
414.0
+13.5%
2048in / 2048out
1,535
1,690
−9.2%
4096in / 4096out
1,622
1,826
−11.2%
Short-output (128out): matches or exceeds paper (±14%) — prefill-dominated, WSE-3 prefill is fast
Long-output (2048/4096out): 9–15% below paper — decode-dominated; paper benchmarked on WSE-2